## Slide 1: Chapter 4: Remote Sensing Spectral Reflectance

## Slide 3: Remote Sensing in Precision Agriculture

## Slide 4: Remote Sensing
The science and art of obtaining information about an object, area, or phenomenon through the analysis of data acquired by a device that is not in contact with object, area, or phenomenon under investigation.

## Slide 5: Four Divisions of Remote Sensing
Remote Sensing can divide into four stages or division based on altitude of the sensor.
  Ground Observation - approximately 0 - 50 ft.
  UAV-UAS - <400 ft
  Low Altitude Airplane - <10,000 ft
  High Altitude Airplane - > 10,000 ft
  Satellite > 150 miles

## Slide 6: Advantages of Ground Level Sensors
Lowest per unit cost
With a self-contained light source, have complete control over incident light, which simplifies calibration and correction.
Ability to collect data at any time.
Potential for very high resolution data collection.
Data can be easily georeferenced for use in a GIS .

## Slide 7: Disadvantages of Ground Level Sensing
Relatively high costs to scan large areas unless part of another field operation.
Cannot simultaneously scan entire fields.

## Slide 8: Turf Scanned with OSU Sensor
100.00
200.00
300.00
400.00
100.00
200.00
300.00
400.00
500.00
600.00
700.00
0.15
0.20
0.25
0.30
0.35
0.40
0.45
0.50
0.55
0.60
0.65
0.70

## Slide 9: OSU/Patchen Active Lighted Sensor with GPS Mounted on an ATV

## Slide 10: 40 ac of Wheat Pasture Center Scanned with ATV

## Slide 11: Interpolated Surface from ATV Scanned Data

## Slide 12: Wheat Pasture Center Scanned with 6 ATV Mounted GreenSeeker Sensors 3/6/2006

## Slide 13: Minnesota Sugar Beets Sensed While Topping

## Slide 14: Wheat Field at Red Rock, OK 2004

## Slide 15: OSU GreenSeeker Sensor Applicator RedRock, OK

## Slide 16: Advantages of Aerial Remote Sensing
Can quickly scan large area.
Cost/ac when scanning large areas is relatively low.
Data can be collected at high resolution < 1m.
User has some control over when data are collected.

## Slide 17: Disadvantages of Aerial Remote Sensing
Images must be rectified and georeferenced.
Cost to scan small areas is high.??
Data can’t be collected at night or in bad weather.
Radiometric calibration must be performed on the images for temporal comparisons.

## Slide 18: Duncan Tech 3 Band Digital Camera and Cessna 172 Airplane

## Slide 19: Camera Mount and Fairing

## Slide 20: NDVI of OSU Experiment Station 1m Resolution

## Slide 21: Detail of Southwest Corner

## Slide 22: False Color Image Noble Foundation Red River Ranch Illustrating Slope Aspect and Bi-directional Reflectance

## Slide 23: False Color (green, red, NIR) Image < 1 m Resolution - Raw Radiometric Data (Courtesy F. Schiebe, SST Development Group)

## Slide 24: False Color (green, red, NIR) Image < 1 m Resolution – Reflectance Corrected Radiometric Data (Courtesy F. Schiebe SST Dev.)

## Slide 25: Gray Scale Image < 1 m Resolution – Reflectance Corrected NDVI (Courtesy F. Schiebe, SST Dev. Grp.)

## Slide 26: Reflectance Corrected Gray Scale Image < 1 m Resolution – Green to Near Infrared Ratio (Courtesy F. Schiebe, SST Dev. Grp.)

## Slide 27
False Color
False Color Reflectance Corrected
Reflectance Corrected Gray Scaled NDVI
Reflectance Corrected Green/NIR

## Slide 28: 1 m False Color (G, R, NIR) Aerial Imagery taken at 5000 ft Marshall, OK

## Slide 29: Advantage of Satellite Sensing
Historical data are readily available.
Cost/ac of large area images is vary low.
Very large areas can be scanned nearly instantaneously.
Data for radiometric bands up to 16 micro meters are available.

## Slide 30: Disadvantages of Satellite Sensing
Resolution is lower than other sources.
Cannot control when an area is scanned, e.g. Landsat scans each area is scanned every 16 to 26 days.
*2-3 days in the future
Correction of radiometric data is challenging because of atmospheric interference.

## Slide 31: Remote Sensing System Measures of Performance
Spatial Resolution
Spectral Response
Spectral Resolution
Frequency of Coverage

## Slide 32: Landsat Satellite Program
United States NASA satellites
Images from Landsat 4 through 7 available from USGS, Sioux Falls, South Dakota
http://eros.usgs.gov/products/satellite.html

## Slide 33: NASA Landsat Web Site

## Slide 34: Landsat Satellites
Landsat Scene - 185 km x 185 km
TM quantatization range 256 (8 bits)
16 day repeat cycle per satellite
Currently only one satellite is operational
Satellite crosses the equator at 9:45 local time (North to South Pass)

## Slide 35: Sensor Used on Current Landsat Satellites

## Slide 36: Landsat Thematic Mapper (TM)
Landsat 5

## Slide 37: TM Spectral Bands

## Slide 38: Landsat TM Bands

## Slide 39: Landsat TM Bands

## Slide 40: TM Image North Central Oklahoma April, 1998

## Slide 41
April 23,1998 TM Scene over North Central Oklahoma

## Slide 42: Systeme Pour l’Observation de la Terre (SPOT)
Orbit repeats every 26 days
60 km wide field-of-view per camera or 117 km field of view with both units
Three satellites 832 km above the earth
Orbits earth every 101 minutes
Sun synchronous orbit

## Slide 43: Systeme Pour l’Observation de la Terre (SPOT)
Quantatization range 256 (8 bits)
Images available through www.spot.com
http://www.spotimage.fr/html

## Slide 44: Systeme Pour l’Observation de la Terre (SPOT)
SPOT Satellites 1, 2, and 3

## Slide 45: Systeme Pour l’Observation de la Terre (SPOT)
Panchromatic
Green 0.50 - 0.59
Red 0.61 – 0.68
NIR 0.78 – 0.89
SWIR 1.58 - 1.75
Spectra in μ m
5 m Resolution
10 m Resolution
10 m Resolution
10 m Resolution
20 m Resolution
SPOT 5

## Slide 46: SPOT XS image

## Slide 47: SPOT Pan image

## Slide 48: Indian Research Satellite IRS - LISS 3 Satellites
23 m Resolution 4 bands
5 m Resolution - Panchromatic
142 by 145 km Image Size
24 day repeat cycle
Images available through Space Imatging (EOSAT) at www.spaceimaging.com

## Slide 49: IRS-LISS

## Slide 50: IRS – LISS Tuscson AZ Airport

## Slide 51: IKONIS
Resolution
  4 m multispectral
  1 m panchromatic
Scene size is approximately 7 miles by 7 miles
Scenes are available from Space Imaging
Farm size images marketed by Earthscan Network, a subsidiary of DTN

## Slide 52: IKONIS RGB Image Covington, OK

## Slide 53: IKONIS False Color G,R,NIR

## Slide 54: IKONIS Panchromatic

## Slide 55: IKONIS 160 ac Field

## Slide 56: Aerial 1m Resolution

## Slide 57: Ball Aerospace –QuickBird 2
Scene Size Approximated 16.5 by 16.5 km
Bands:
  Panchromatic – 70 cm resolution
    B & W 450-900 nm
  Multispectral – 2.8 m resolution
    Blue 450-520 nm
    Green 520-600 nm
    Red 630-690 nm
    NIR 760-900 nm
Quantatization range 8 or 16 bits
Positional Accuracy
    23 m 90% CE 14 m RMSE

## Slide 58: QuickBird Example From Digital Globe
http://www.digitalglobe.com/

## Slide 59: Steps to Utilize Remote Sensed Data (modified from JD text
Collect data
Process image data (rectification, radiometric correction, and georeferencing)
Examine image and analyze statistical data
Perform ground truthing of remote-sensed data

## Slide 60: Steps to Utilize Remote Sensed Data (modified from JD text)
Incorporate remote sensed and ground truth data into a GIS
Develop calibration equations for remote sensed data
Identify cause-effect relationships among measured variables and crop conditions
Treat regions in fields (management zones) based on information generated

## Slide 61: GreenSeeker/IKONIS Imagery

## Slide 62: Marshall Farm

## Slide 63: N Rich Strip

## Slide 64: Large Area Unedited Data

## Slide 65: Large Area NDVI Edited

## Slide 66: Large Area as Applied N

## Slide 67: April 1998 Landsat 5 TM Near Marshall, OK

## Slide 68: IKONIS Image Near Marshall, OK

## Slide 69: IKONIS Near Marshall, OK
N Rich Strip
No P Strip

## Slide 70: Near Marshall, OK - IKONIS NDVI

## Slide 71: GreenSeeker NDVI and IKONIS False Color

## Slide 72: Cassidy GreenSeeker/IKONIS

## Slide 73: Mapping Sensor Data

## Slide 74: Images and Values
Visible: True color, You see what is reflected.
False Color: Opposite of true color. A false-color image sacrifices natural color rendition (in contrast to a true-color image) in order to ease the detection of features that are not readily discernible otherwise
Vegetative Index:
NDVI: Indices, Calculation based on reflectance
Dozens if not 100’s of Indices.

## Slide 75: True vs False

## Slide 76: Vegetative Indices
VT: Up and down for: 550, 590, 650, 780, 920, 940, 970 and one more
OSU: 590, 650, 780, 920, 970 maybe 680
theOSU: Biomass - 780,680, maybe 650
CTD, WI - 970,920, maybe 900,880, 850
N - 780,740, maybe 680, 700
650, 780, 920, 970
590, 680

## Slide 77: Issues in conducting remote sensing
  Variability in light source
  Filtering of light along path
  Measuring units/calibration of sensing system
  Geometry
  Spatial and temporal frequency of measurements
Light
Source
Plant or Soil
Surface
Reflected Light
Sensing
System

## Slide 78: Fundamentals of Light
Light = Energy (radiant energy)
  Readily converted to heat
    Light shining on a surface heats the surface
    Heat = energy
Light = Electro-magnetic phenomena
  Has the characteristics of electromagnetic waves (eg. radio waves)
  Also behaves like particles (e.g.. photons)

## Slide 79: Photo-Chemistry
Light may be absorbed and participate (drive) a chemical reaction. Example: Photosynthesis in plants
The wavelength must be correct to be absorbed by some participant(s) in the reaction
Some structure must be present to allow the reaction to occur
Chlorophyll
Plant physical and chemical structure
Notes: 14
15

## Slide 80: Visual reception of color
Receptors in our eyes are tuned to particular photon energies (hn)
Discrimination of color depends on a mix of different receptors
Visual sensitivity is typically from wavelengths of ~350nm (violet) to ~760nm (red)
Wavelength
400 nm
700 nm
500 nm

## Slide 81: Silicon Responsivity
Notes: 21
18

## Slide 82: Primary and secondary absorbers in plants
Primary
  Chlorophyll-a
  Chlorophyll-b
Secondary
  Carotenoids
  Phycobilins
  Anthocyanins

## Slide 83: Chlorophyll absorbance
Chla: black
Chlb: red
BChla: magenta
BChlb: orange
BChlc: cyan
BChld: bue
BChle: green
Source: Frigaard et al. (1996), FEMS Microbiol. Ecol. 20: 69-77

## Slide 84: Absorption of Visible Light by Photo-pigments
Sunlight
Intensity
Phycocyanin
300 400 500 600 700 800
Wavelength, nm
B-Carotene
Absorption
Chlorophyll a
Chlorophyll b
Lehninger, Nelson and Cox

## Slide 85: Radiation Energy Balance
Incoming radiation interacts with an object
and may follow three exit paths:
  Reflection
  Absorption
  Transmission
a + t + r = 1.0
a, t, and r are the
fractions taking each path
Known as absorbance,transmittance, reflectance respectively
Il0 a
Il0 t
Il0 r
Il0

## Slide 86: Nature of absorption by the atmosphere
Incident
Reflected
Transmitted
Absorbed
Radiant energy balance must
be computed for each
component of the atmosphere
and for each wavelength
to estimate the radiation
incident on the earth's surface
Earth's
surface
Atmosphere

## Slide 87: Reflectance
  Ratio of incoming to reflected irradiance
  Incoming can be measured using a “white” reflectance target
  Reflectance is not a function of incoming irradiance level or spectral content, but of target characteristics

## Slide 88: Solar Irradiance
NIR
UV

## Slide 89
Plant Reflectance
Wavelength (nm)
Reflectance (%)
0.25
0.5
Visible
Near Infrared
450
550
650
750
850
950
1050
500
600
700
1000
900
800
0.00
PhotosyntheticPotential
Measure of living plant cell’s ability to reflect infrared light
Indicator of Available Chlorophyl

## Slide 90: Spectral Response to Nitrogen
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
400
500
600
700
800
Wavelength, nm
Reflectance
0 Nitrogen
100 lb Nitrogen/ac
Winter Wheat at Feekes 5 in potted soil
Measure of living plant cell’s ability to reflect infrared light
Photosynthetic Potential

## Slide 91: Soil and crop reflectance

## Slide 92: Interfering Inputs: Soil Reflectances - Oklahoma

## Slide 93: Irradiance Indices
Spectral shift in illumination
prevents use of
simple irradiance sensing
Based on ratios of reflected
Red and NIR intensity
Example Index:
Rred / Rnir

## Slide 94: Reflectance Indices
Based on ratios of Red and NIR Reflectance
Red Reflectance:
rred = Rred / Ired
Reflectance is primarily
a function of target
NIR Reflectance:
rnir = Rred / Ired
Vegetative Index:

## Slide 95: Simple Ratio
Calculated the reflectance values of Red and NIR
Varies from 0 to 1
Measure of leaf area
  Can be used as a leaf area index
Related to other agronomic/botanical measures
  Biomass
  Chlorophyll
  Nitrogen
  Yield

## Slide 96: NDVI
Normalized Difference Vegetative Index
Developed as an irradiance index for remote sensing
Varies from -1 to 1
    Soil NDVI = -0.05 to .05
    Plant NDVI = 0.4 to 0.9
    Typical plants with soil background NDVI=0.3-0.8
NDVI from different sources vary
  Bandwidths for Red, NIR vary
  Irradiance vs. reflectance based

## Slide 97: Normalized Difference Vegetative Index - NDVI
Calculated from the red and near-infrared bands
Equivalent to a plant physical examination
Correlated with:
  Plant biomass
  Crop yield
  Plant nitrogen
  Plant chlorophyll
  Water stress
  Plant diseases
  Insect damage

## Slide 98
GreenSeekerTM Sensor Light Detection and Filtering
Detection of
Reflected
NIR and RED
+Sun
Target
NIR and RED
Modulated
Illumination
Direction

## Slide 99: Sensor Function
Light
generation
Light signal
Light
detection
Valve settings
?
Calculate NDVI
?
Lookup valve setting
?
Apply valve setting
?
Send data to UI
“Sensor”
Valves and Nozzles

## Slide 100: Equipment
Active v Passive
Active Handhelds
  Limited wavelengths
  Ease of use
Passive sensors
  “Unlimited” wavelegths
  Limitation on use
  Can have sensor/s for both NUE and WUE
  Calibration
    Down view only, constant calibration
    Down + up view, 1 to 2 calibrations per day.

## Slide 101: FieldSpec® HandHeld 2™ Spectroradiometer
Weighs Approx 1 lb.
Full Spectrum
Down facing only

## Slide 102: MSR16R
16 Band Max
Up and down facing.

## Slide 103: Cropscan
http://www.cvmt.dk/projects/Across/Foulum_13_May_2004.html