## Slide 1: Global Positioning System

## Slide 2: The History of GPS
Feasibility studies begun in 1960’s.
Pentagon appropriates funding in 1973.
First satellite launched in 1978.
1990’s Used in Persian Gulf War
System declared fully operational in April, 1995.
Department of Defense (DoD)

## Slide 3: Three Segments of the GPS
Control Segment
Space Segment
User Segment
Monitor Stations
Ground Antennas
Master Station

## Slide 4: Four Basic Functions of GPS
Position and coordinates.
The distance and direction between any two waypoints, or a position and a waypoint.
Travel progress reports.
Accurate time measurement.

## Slide 5: NAVSTAR, Space Segment
24+ Birds
24 Active 4 Spare
  Consistently repaired/replaced.
6 paths or plates
12 hr orbit
2 or 3 atomic or nuclear clocks,
  2/2 cesium rubidium; now 3 rubidium

## Slide 6: Control Sector
Several Monitoring Stations
1 Master Control
  Colorado Springs Co.
MC, computes clock errors tracks orbits. Sends corrective info back to satelite.

## Slide 7: User Segment
Military.
Search and rescue.
Disaster relief.
Surveying.
Marine, aeronautical and terrestrial navigation.
Remote controlled vehicle and robot guidance.
Satellite positioning and tracking.
Shipping.
Geographic Information Systems (GIS).
Recreation.

## Slide 8: Satellite Ranging.
Each satellite transmits
  Position
  Timing

## Slide 9: Position is Based on Time
T + 3
Distance between satellite and receiver = “3 times the speed of light”
T
Signal leaves satellite at time “T”
Signal is picked up by the receiver at time “T + 3”

## Slide 10: Pseudo Random Noise Code
Receiver PRN
Satellite PRN
Time Difference

## Slide 11: Real Time Differential GPS
DGPS Site
x+30, y+60
x+5, y-3
True coordinates = x+0, y+0
Correction = x-5, y+3
DGPS correction = x+(30-5) and y+(60+3)
True coordinates = x+25, y+63
x-5, y+3
DGPS Receiver
Receiver

## Slide 12: Good Satellite Geometry

## Slide 13: Poor Satellite Geometry

## Slide 14: Poor Satellite Geometry

## Slide 16: Accuracy and Factors Affecting it
Satellite Clocks
Satellite Ordit
Earths Atmosmphere
Multi-Path Errors
GPS Reciever

## Slide 17: # of Satellites Needed.

## Slide 18: DGPS
Differential Correction.
1 or more stationary GPS receivers located at surveyed positions.
Typical Error GPS DGPS Clock 3-8ft <1ft Orbit 3-8 <1 Lanoshpere 6.5-16 1.4 Tropo 1.6-3.3 .7 Multipath 1.6-5 1.6-5 Reciver Noise 1-3 1-3

## Slide 19: Sources of Real-Time DGPS
Nationwide Differential DGPS, (U.S. Coast Guard Beacon System)
Local Base Station, User Supplied
Satelitte-based differential Corrections (WAAS, Starfire®, OminiSTAR®, ect.

## Slide 20: USCG Radio Beacon
285kHz-325 kHz

## Slide 21: Local base Station
900 MHz-2.4GHz, Am or Fm Style (50-60 miles)
RTK- Real Time Kinematic
Centimeter Accuracy
http://www.precisepath.com/​

## Slide 22: Satellite-Based DGPS
WAAS, Starfire®, OminiSTAR®
Geo-Stationary Satellites
Orbits keeps it over the same point on the ground.
Orbits the same speed as Earths Rotation
Commonly used for TV broadcast.

## Slide 23: WAAS
Wide Area Augmentation System (WAAS) is an air navigation aid developed by the Federal Aviation Administration (prime contractor Raytheon Company) to augment the Global Positioning System (GPS),
WAAS uses a network of ground-based reference stations, in North America and Hawaii, to measure small variations in the GPS satellites' signals in the western hemisphere.
The WAAS specification requires it to provide a position accuracy of 7.6 metres (25 ft) or better (for both lateral and vertical measurements), at least 95% of the time.[2] Actual performance measurements of the system at specific locations have shown it typically provides better than 1.0 metre (3 ft 3 in) laterally and 1.5 metres (4 ft 11 in) vertically throughout most of the contiguous United States and large parts of Canada and Alaska.[3] With these results, WAAS is capable of achieving the required Category I precision approach accuracy of 16 metres (52 ft) laterally and 4.0 metres (13.1 ft) vertically.[4]

## Slide 24
Wide Area Augmentation System
Geostationary WAAS satellites
GPS Constellation
WAAS Control Station (West Coast)
Local Area System (LAAS)
WAAS Control Station (East Coast)

## Slide 25
WAAS Reference Station Barrow Alaska

## Slide 26
How good is WAAS?
+ - 3 meters
+-15 meters
With Selective Availability set to zero, and under ideal conditions, a GPS receiver without WAAS can achieve fifteen meter accuracy most of the time.*
Under ideal conditions a WAAS equipped GPS receiver can achieve three meter accuracy 95% of the time.*
* Precision depends on good satellite geometry, open sky view, and no user induced errors.

## Slide 27: Others
StarFire – John Deere (approx $800 annual)
Omni-Star- American Mobile Sat Corp. (
GLONASS- Russia’s Global Nav
GALILEO- European Space Agency

## Slide 28
Love this Pic

## Slide 30
http://soil4213.okstate.edu/2011/Student_Presentations2011.htm
NAVSTAR http://spaceandtech.com/spacedata/constellations/navstar-gps_consum.shtml
Some slides adopted from Charlie Leonard, 1999 (revised 2001, 2002)