## Slide 1: Wesley M. Porter Extension Irrigation Specialist
Variable Rate Irrigation
Pork and Dairy Farms

## Slide 2: What If We Had the Ability To:
Develop Irrigation Management Zones
Apply correct and relevant amounts of irrigation to these zones
Apply no water to non-cropped areas
The Solution is Variable Rate Irrigation

## Slide 3: Variable Rate Irrigation
Variable Rate Irrigation also known as VRI or Precision Irrigation
The controlled application of irrigation water over a particular area, based on observed or measured conditions.
  Varied rates
  On/Off
Scheduling Rates based on perceived or measured water requirements of sub-field zones:
  Soil Moisture Sensors
    Resistive or Capacitance
  Leaf Canopy Sensors
  Remote Sensing

## Slide 4: Variable Rate Irrigation
In this case the predominate use will be to control the irrigation system on/off over particular areas:
  Wet Areas
  Overlapping Areas
  Non-Crop areas (Roads, Structures, waterways, ditches etc.)
  Sensitive Areas
  Field Variability

## Slide 5: Variable Rate Irrigation: Wet Areas

## Slide 6: Variable Rate Irrigation: Overlap

## Slide 7: Variable Rate Irrigation: Non-Crop Areas
Non-Crop Area: House or building

## Slide 8: Variable Rate Irrigation: Variability

## Slide 9: Variable Rate Irrigation: Variability

## Slide 10: Variable Rate Irrigation: Variability

## Slide 11: Variable Rate Irrigation: Variability
Drainage
Ditches
Heavier,
Wetter Soil
Lighter,
Drier Soil

## Slide 12: Variable Rate Irrigation: Variability
Overlapping
Pivots
Non-cropped
Area

## Slide 13: How Does VRI Work?
Retrofits onto existing center pivot/lateral systems
Integrates GPS positioning into a control system
Control system cycles individual sprinklers or groups of sprinklers ON & OFF (duty cycle, seconds ON per minutes).
System travel speed

## Slide 14: How Does VRI Work?
A VR system requires:
  A control system for each developed zone
    Can consist of electronic or pneumatic valves
  A control software for inputting the developed zones and supplying a control signal
  Differential GPS (for accurate location of the system)
  Either a variable frequency pump or pressure relief to account for changes in flow and pressure due to varying zones.

## Slide 15: How Does VRI Work?
The controller uses the speed for the max rate required for the current zones and cycles the rest of the zones as a percentage of this rate.

## Slide 16: VRI

## Slide 17: VRI

## Slide 18: System Calibration
Little to no input needed from the user.
Can do a uniformity check.
  http://www.caes.uga.edu/publications/pubDetail.cfm?pk_id=7685
The software should handle the flow rate of the system as long as nozzles are properly sized.
Can check speed vs. application rate for calibration.

## Slide 19: Potential Benefits
Save Water
Prevent double application
Improve irrigation management decisions
Improve efficiency (under- or over- watering)
Reduce weeds in non-cropped areas
Reduce nutrient leaching
Reduce disease in some crops
Reduce/optimize pumping costs
Increase yields
Regulatory Benefits

## Slide 20: Reasons for Utilizing VRI

## Slide 21: No Water Zones
Non-cropped areas not watered
Environmentally sensitive areas not watered
Overlapping pivots

## Slide 22: Non-cropped Areas

## Slide 23: Non-cropped Areas

## Slide 24: Non-cropped Areas

## Slide 25: Topographical/Soil Variability

## Slide 26: Non-cropped Areas

## Slide 27: Off-Site Applications

## Slide 28: Potential Benefits in Manure Applications
Fine tune waste water application
Reduce or eliminate effluent application to environmentally sensitive areas
More precisely apply effluent adjacent to buffers or “setback” zones.
Increase water use efficiency
Optimize nutrient management

## Slide 29: Is VRI Relevant to My Operation?
Your farm’s irrigation system could benefit from VRI if your field has:
  Environmentally sensitive areas under the system coverage area (end gun or nozzles)
  Different nutrient management zones
  Non-cropped areas under pivot coverage
  Varying soil types

## Slide 30: VRI Components

## Slide 31: VRI Components
Controllers

## Slide 32: VRI Components
GPS Receiver

## Slide 33: VRI Components
Node/Zone Circuits and Solenoids

## Slide 34: VRI Components
Flow Control Valves
(can be actuated via pneumatics or hydraulics)

## Slide 35: VRI Components
Compressed air supply

## Slide 36: VRI Components
Compressed air supply
X
X
Most commercial systems use water from mainline in fresh water installations.

## Slide 37: VRI Zone Development
Equipment widths
Soil EC
Soil Type
Elevation
Field Size
Irrigation Tower Length
Crops produced in field (single or multiple crops)
Other typical precision agriculture zone development tools.

## Slide 38: VRI Zone Development
How large do I want my management zones?
  What is feasible for my operation?
  What type of field resolution do I want?
  How long is my irrigation tower?
  How many nozzles do I have?
  How wide do the management zones need to be?
  The higher the resolution the more control equipment required.
  Two nozzles per zone would be the minimum.
  Keep in mind that smaller zones can be treated uniform and “merged”, but larger zones cannot be divided once the control system is implemented.

## Slide 39: VRI Zone Development
How am I currently scheduling my irrigation?
  Using VR will require a more intensive management and scheduling strategy.
  Moisture sensors in every zone? In similar zones?
  Do I want to work towards an automated system or would I be better off calculating and entering each zones needed rate separately?

## Slide 40: Application Map/Zone Development

## Slide 41: Application Map/Zone Development
Low, wet spot
Wet drainage spot
Dry, sandy spot
Overlapping pivot
Wetland area

## Slide 42: Applications

## Slide 43: Applications

## Slide 44: Applications

## Slide 45: Applications

## Slide 46: Applications

## Slide 47: Applications

## Slide 48: UGA Dairy Pivot-Tifton Campus

## Slide 49: UGA Dairy Pivot-Tifton Campus
3rd tower sprinklers cycling
4th tower sprinklers OFF

## Slide 50: NRCS Cost Share Example
Retrofit of and Existing Sprinkler System for water conservation:
  $4.34 per linear foot
Variable Rate Irrigation Retrofit
  $15.44 per linear foot
These are estimates and not representative of actual NRCS cost shares.
Contact your local NRCS office for exact cost share in your region and options for your particular situation

## Slide 51: Questions/Comments?