## Slide 1: Variable Rate Application
Randy Taylor
Biosystems and Agricultural Engineering
Oklahoma State University

## Slide 2: Field Scale Variability
Macro-variability
  Likely tied to soil type, landscape position, or something else
Micro-variability
  Could be sub meter or even individual plants

## Slide 3: Variability View from Equipment
Longitudinal
  Down-the-row
  Response time issues
Lateral
  Across the boom
  Boom divisions
A greater distance between the control and delivery points means a lower resolution and increased scale.

## Slide 4: Variable Rate Management
What measurements will be used to identify within-field variation in nutrient (if nutrient input is to be varied) supply or availability?
  The basis for variable rate inputs
What input recommendation or base input rate will be used?
What management scale will be used?

## Slide 5: Sensor v. Map Based VRA
In a map based system, the controller receives a rate change as the applicator crosses into a new zone or application grid (step changes).
However, with a sensor based system the controller typically receives an updated rate every second and does not have the opportunity to stabilize.

## Slide 6: Map-Based
Determine management scale
Apply diagnostic tools to develop prescription
Develop prescription map for the field
  Zone creation/sampling
  Grid sampling/scale
  Yield data/goal/stability
  Variable rate input prescription map

## Slide 7: Map-Based Decision Inputs
Soil testing
Remote sensing of crop and soil properties
Site-specific data from yield monitors
Soil electrical conductivity maps
On-farm research trials
Other information?

## Slide 8: Traditional Nitrogen Approach
N recommendation = yield goal x 1.2 – N credits

## Slide 9: Spatial Yield Goals
Start with multiple yield maps on the same field.
Do they need to be the same crop?
Normalize each year and average the maps.
Does yield stability matter?

## Slide 10: Multi-Year Yield History

## Slide 11: Mean Relative Difference
A normalization method where the mean value is subtracted from the local value.
Data are aggregated into cells before subtracting the mean.
Variability of a cell over time tells us if it is stable or unstable
This method gives a better opportunity to classify consistently low or high yielding areas
Find areas where like classed cells are spatially contiguous

## Slide 12: ‘Whisker Plots’ of YM Data
Points are the mean relative difference for each cell
Bars are the standard deviation of yield through time.

## Slide 13: Relative Difference Map
Based on 6 crops in 4 years of yield data.
Corn-Wheat-DC Soybeans
Yellow is within +/-10% of the mean.
Green is at least 10% above average and orange is at least 10% below average.

## Slide 14: Yield Stability
Mean Relative Difference
Yield Classes

## Slide 15: Yield Stability

## Slide 16: In-Field Response
Schmidt, J.P., A.J. DeJoia, R.B. Ferguson, R.K. Taylor, R.K. Young, and J.L. Havlin. 2003. Corn Yield Response to Nitrogen at Multiple In-Field Locations. Agron. J. 94:798–806.
“The results presented here indicated that there was, in most cases, significant variability in grain yield response to increasing N rates among in-field locations. The minimum N rate corresponding to maximum corn yield was as low as 52 kg N / ha and as high as 182 kg N / ha, considering all locations across three fields in this study. However, variability in yield responses to N was not consistently related to soil OM content.”

## Slide 17: Management Zones
Inman, D., R. Khosla, D. G. Westfall, and R. Reich. 2005. Nitrogen Uptake across Site Specific Management Zones in Irrigated Corn Production Systems. Agron. J. 97:169–176 (2005).
“Grain yield response to N was also shown to be significantly different across management zones. This study showed that spatially variable crop parameters could potentially be managed using SSMZs.”

## Slide 18: Traditional Method – Smaller Scale
Ferguson, R.B., G.W. Hergert, J.S. Schepers, C.A. Gotway, J.E. Cahoon, and T.A. Peterson. 2002. Site-Specific Nitrogen Management of Irrigated Maize: Yield and Soil Residual Nitrate Effects. Soil Sci. Soc. Am. J. 66:544–553.
“Over 13 site-years, no consistent benefit (either increased yield or reduced soil residual NO3-N) was observed with variable rate N application. There was no disadvantage to using variable rate N application in terms of N applied or grain yield, but no advantage that would justify the cost and effort of variable rate application with procedures used in this study.”

## Slide 19: Traditional Recommendations
Traditional recommendations are typical very ‘coarse’ and were developed for wider geographic regions (maybe even statewide).
Applying these on smaller scales (sub-field) may not be sufficient to see a response.
True site-specific response functions will be generated on site.

## Slide 20: Sensor-Based
Measure crop status in the field
Apply input at variable rates to meet crop needs
Need to relate the measurement to the crop need

## Slide 21: Prescriptions
There are three inputs that are currently being VR applied for cotton
  Plant growth regulators
  Defoliants and boll openers
  Nitrogen
Where will you get your prescription?
  Land Grant
  Industry
  Home Grown

## Slide 22: Sensor-Based Decision Inputs
Plant or canopy reflectance
Chlorophyll measurements
On-the-go or remotely sensed crop canopy imagery
Pre-selected N prescription
In-field reference strip may be needed

## Slide 23: Normalized Difference Vegetative Index - NDVI
Calculated from the red and near-infrared bands
Equivalent to a plant physical examination
Correlated with:
  Plant biomass
  Crop yield
  Plant nitrogen
  Plant chlorophyll
  Water stress
  Plant diseases
  Insect damage
Varies from -1 to 1
  Soil NDVI = -0.05 to .05
  Plant NDVI = 0.4 to 0.9
  Typical plants with soil background NDVI=0.3-0.8
NDVI from different sources vary
  Bandwidths for Red, NIR vary
  Irradiance vs. reflectance based

## Slide 24: Sensor Configurations

## Slide 25: Sensor Based Nitrogen Management

## Slide 26: Rate Controllers and Tuning
Prescriptions should not be developed without considering rate controller performance.
Worry about the macro variability within the field.
Are you capturing the general trend?

## Slide 27: Challenges
Measuring differences at larger scales
  Non uniform plots
Matching application and harvest equipment
Harvesting plots
Managing data with potential errors

## Slide 28: Equipment

## Slide 29: Liquid Systems
Most commercial rate controllers can be set to about a 2 second response time.
Multiple control sections will require multiple control valves and possibly flow meters.
Pulse width modulation and binary valve systems have promise.

## Slide 30: Typical Controller Adjustments
Valve Speed
  May be the only adjustment
Brake Point
  When do you start slowing down
Dead-Band
  How good is good enough?

## Slide 31: Setting Valve Speed

## Slide 32: Brake Point (~Damping)
Do your passengers ride with a hand on the dash?

## Slide 33: Underdamped System
As-Applied Data from Mid-Tech TASC-6200

## Slide 34: Dead-Band
Range where adjustment is deemed unnecessary (within a tolerable range of the target).
2% Dead-Band

## Slide 35: Raven 440 with PWM

## Slide 36: Importance of Valve Settings
10% Brake Point
2% Dead-Band
40% Brake Point
3% Dead-Band

## Slide 37: Variable Rate Liquid Applicators
Direct Injection
  Complex
  Time lag
Fixed orifice nozzles
  Flow proportional to square root of pressure
  Difficult to achieve range in flow rates
Pulse Width Modulation
Variable orifice nozzles
  Pressure/Flow relationship is more complex

## Slide 38: Orifice Metering

## Slide 39: What PWM Does
Allows control of both nozzle pressure and flow independently
Increases the effective operating range by a factor of 4 (8:1 versus 2:1) compared to fixed orifice nozzles.
Controls flow by pulsing the nozzle.
Even coverage using blended pulse technology
SHORT ON TIME = LOW FLOW RATE
LONG ON TIME = HIGH FLOW RATE

## Slide 40: Nozzles and Rate Changes
Variable orifice nozzles open up as flow to the nozzle increases. This results in a greater flow for a given pressure and a much wider flow range.

## Slide 41: Nozzle Tests

## Slide 42: TurboDrop VR
Nozzles 5 and 19 over applied at all flows
Nozzle 30 over applied at low and medium flows
No nozzles under applied at medium and high flows
More variability at low flow

## Slide 43: VeriTarget
Five nozzles over applied at low flow while two under applied.
At medium and high flows the tendency was under application but overall performance was better.

## Slide 44: Granular VRT
Granular distribution/delivery systems follow two basic designs
  Gate/belt or chain/spinner
  Metering wheel/air boom
While both systems can be used for variable rate application, reducing the application scale to a partially width is really not feasible

## Slide 45: Spinner Spreaders
Reducing application scales with spinner spreaders is really not feasible.
The material is centrally metered and distributed.
Furthermore, VRA with spinner spreaders is a challenge.
  Spread distribution patterns are typically a function of flow rate onto the spinner

## Slide 46: Air Boom Systems
The material is centrally metered, but patterns are created locally.
The primary challenge is lag time from the metering system to the point of application

## Slide 47: Application Error During Turns
OmniRow from Raven for planters
Pinpoint Control from Capstan Ag Systems
  Static tests with simulated turns and speed (12 mph).
  Application rate was 10 GPA

## Slide 48: TCS Evaluation
Measured and target nozzle flows for a 120 foot boom in left and right turns. The turn radius is 90 foot.
Simulated Test Path

## Slide 49: Population Variability

## Slide 50: Relationship to Turn Radius

## Slide 51
Randy Taylor
Randy.Taylor@okstate.edu
405-744-5277
Questions